## Slide 1: Wireshark at Enterprise Scale
Stephen Donnelly
endace

## Slide 2: Agenda
Why We Capture
How We Capture
How We Scale

## Slide 3: Why: Who is it for
NetOps
SecOps
DevOps

## Slide 4: Why: Application team
Owns the applications
Responsible for application availability and performance
  Business Critical Infrastructure and Services
Troubleshooting Application Issues
  Has access to server and application logs
  Rely on Network
Request Packets for advanced troubleshooting

## Slide 5: Why: Network team
Owns the network
  Has access to network infrastructure
  Controls switching, routing, and firewalls
Responsible for Network availability and performance
Monitoring for network layer issues
  High-level SNMP statistics
  NetFlow/IPFIX
Packets for advanced troubleshooting

## Slide 6: Why: Security team
Responsible for securing the enterprise
Network monitoring for security
  Detect intrusions, IOCs, threats, vulnerabilities
  May rely on NetOps for access or response
Need full packet capture in real-time (DPI)
  Signature detection (IDS)
  Behavioural Analysis (NBAD)
Packet capture and retention for incident analysis

## Slide 7: Why: what you can’t do without Packets
Collect and examine evidence
  Requests and responses
  Actual data transferred
Develop and test rules/signatures/ACLs
Debug network/transport layer issues
  Protocol and application errors
  Timing issues, packet loss, latency, microbursts
Regulatory compliance

## Slide 8: Why: Enterprise Challenges
Scale
  Multiple distributed capture points
  High speed links
  Huge data volumes
  History vs Cost
Comprehension
  Visualisation
  Indexing
  Search

## Slide 9: Agenda
Why We Capture
How We Capture
How We Scale

## Slide 10: How: Types of capture
On Demand
Live Inspection
Triggered Recording
Continuous Recording

## Slide 11: How: On-demand capture
Low to no equipment costs
  Open source - Wireshark!
  Existing equipment
High time cost
  Expert staff/consultants
Reactive – no history recorded
  Temporary
  Iterative

## Slide 12: How: Live inspection
Continuous capture without recording
  Permanent dedicated equipment
  Placement affects coverage
Open source – Suricata, Snort, Zeek
Commercial IDS/NBAD/NDR/AI
    Appliance or software model
Logged alerts provide historical summary
  May log individual triggering packet(s)

## Slide 13: How: Triggered recording
Live Inspection plus “Smart” recording
Records only limited subset of traffic based on triggers/alerts
  Less storage space and performance required compared to Continuous Capture
  Trigger criteria determined in advance
    May miss traffic of interest (e.g. Zero Days)
  Limited pre-trigger visibility (buffer depth)

## Slide 14: How: Continuous recording
Capture 100% of packets to disk
  Maintain rotating capture buffer
  Optional filtering/compression
No risk of missing traffic of interest
Storage capacity limits retention time
  Time-to-investigation window
Complementary to live inspection tools
  Potentially co-hosted

## Slide 15: How: Technology
Acquiring packets
Tap/tool placement
Storage requirements
Encryption/decryption
Compression

## Slide 16: How: On-Demand Capture
Capture on end-point
  NIC Offloads
  Time stamp quality
  Heisenberg – observation affects system
Port Mirror/SPAN + laptop
  Many laptops no longer have Ethernet!
  Thunderbolt NIC + NVMe SSD
  Limited capture time
Portable “Sniffers”

## Slide 17: How: Live/Continuous Capture
Dedicated capture/inspection system(s)
Port Mirror/SPAN
  Consumes valuable switch ports
  Limits concurrent tools on same traffic
Passive (or active) TAP
  Single (bidirectional) link at a time
  Maintains timing and packet order
  Check optical link budget

## Slide 18: How: Network Packet Broker
Programmable multi-port device
  Taps multiple links
  Timestamps Packets
  Optional filter, truncate, decrypt
Steers traffic to multiple tools
  Aggregate multiple slower links
  Support multiple tools via duplication
  Load balance traffic to slower tools, or to increase storage capacity

## Slide 19: How: Deployment options
DMZ
LAN
Private
Data Center
Partner Zones
Telecommuters
Core
Switch
Internet
Business Partners
Trusted Zone
Branch Offices
Internal
Firewall
HQ or Private Datacenter
Trusted WiFi

## Slide 20: How: Continuous Capture Storage
Bandwidth over time
  1Gbps = 125MB/s
  125MB/s * 3600s = 450GB/hr
  450GB/hr * 24h = 10.8TB/day
  10.8TB/day * 7d = 75.6TB/week
  Plus indexes and metadata
Network links are bi-directional
  75.6TB/week * 2 = 151.2TB/week!
  At 10Gbps * 2 = 1.512PB/week

## Slide 21: How: Example - REANNZ WAN traffic
Example 10Gbps+ WAN link
  Link asymmetry >4:1
  7-day bi-directional average 2.8Gbps
7-day raw packet total = 212TB
https://weathermap.reannz.co.nz/node.php?src=and09&int=ae0&cf=AVERAGE

## Slide 22: How: Compression
Some network data compresses well
  Packet headers, text, html, JSON…
  Binary compression ratios can be 2:1 or better
Some data is incompressible
  Compressed data (media)
    Detect by file type or payload entropy
  Encrypted data (without keys)
    Detect by TLS or payload entropy
  Can be truncated, keeping packet headers

## Slide 23: How: Compression - payload entropy
Shannon entropy is measured in bits
  0 is highly regular, 8 is totally random
Possible to categorise content types:
  Text ~4-5
  JPEG ~6-7
  Binary compressed >7
  Encrypted >7.5

## Slide 24: How: Compression + Truncation
Incompressible payloads can be truncated
  If they provide little useful information
  Dynamic truncation length based on payload offset rather than fixed snap length
Remaining data compresses well
Combined reduction of 4-10:1 possible
  REANNZ 212TB/week could become 20-50TB/week

## Slide 25: How: Encryption/decryption
Known server keys - Deprecated
  Perfect Forward Secrecy
Logging secrets client-side (SSLKEYLOGFILE)
  Limited coverage
TLS proxy/offload
  Proxy requires trusted CA/re-signing (MitM)
  Crypto offload common for server farms

## Slide 26: Agenda
Why We Capture
How We Capture
How We Scale

## Slide 27: Scale: Comprehension
Fabrics
Capture Metadata
Time Synchronization
Visualization
Search

## Slide 28: Scale: Fabrics
Enterprise scale networks
  Globally distributed
    Datacenters, branch offices, staff
  10-100k+ Devices
  10s-100s of NPBs, Capture Devices
Fabric: distributed capture, storage, search
  Avoid data backhaul
  Centralized search front-end
  Scalability

## Slide 29: Enterprise Fabric
Group A
(SecOps)
Group B
(NetOps)
Group …
IT / Operations
Stack of EndaceProbes
Single EndaceProbe
Single EndaceProbe
Single EndaceProbe
EndaceCMS
InvestigationManager instances
Stack of EndaceProbes
Stack of EndaceProbes

## Slide 30: Scale: Multi-point capture
Coverage
History
Reachability
  Packet Loss determination
Latency
  One-way-delay vs Round-trip
Mutation

## Slide 31: Scale: Capture Metadata
Packets tell us What happened
  Need Who, When, Where, How, Why?
    Who: Multi-tenant, Authorization, Users
    When: Time stamps, Synchronization
    Where: Probe and link details
    How: Capture tools, versions, statistics
    Why: Ticket IDs, alerts, comments
  Critical when capturing at multiple points
May require anonymization when sharing

## Slide 32: Scale: Time Synchronization
High Resolution sufficient for single points
  Round-trip time
  Service response time
Synchronization necessary for multi-point
  One-way delay, latency
  Ordering of packets, events
  Correlation with logs, alerts
Financial industry

## Slide 33: Scale: Visualisation
Visualize network information
  Over time
  Connectivity
  Flows/applications
  Statistics
Based on flow data or indexes
  Accelerate searches

## Slide 35: Scale: Search
How do you find one flow in TBs of packets?
  Time indexes
  Address indexes
  Flow indexes (5-tuple: Addresses, Ports, Protocol)
  Extraction capability -> dissect/download
  Comprehensive indexes can be large
APIs and Integrations for Automation
  REST
  SIEM

## Slide 38: Conclusion: Wireshark in Enterprise
Wireshark is a tremendous analysis tool!
  Unparalleled detail
  2800+ protocols, 228k+ fields
Augmented to Enterprise Scale
  High performance multi-point capture
  Metadata generation and collection
  Indexing and Storage
  Distributed Fabric Search
Perfect combination

## Slide 39: Thank You!
Please fill in your session feedback Survey!
Any questions?
You can contact me on Discord or
stephen.donnelly@endace.com